SEVENTH SEMESTER

ELECTRICAL ENGINEERING

OPTO-ELECTRONIC DEVICES

Prepared By

Khuram Khan

B.Sc Electrical, FUUAST-Islamabad

Checked By

Engr. Zubair Khalid

BSc. Computer Engg. COMSATS attd.

COMMUNICATION LAB

DEPARTMENT OF ELECTRICAL ENGINEERING

Federal Urdu University of Arts, Science & Technology

G-7/1 Islamabad- Pakistan

www.fuuastisb.edu.pk

Name:  ____________________________________________

Registration No: ____________________________________

Roll No: ___________________________________________

Semester: _________________________________________

Batch: ____________________________________________

EXPERIMENT NO. 1

Introduction to optoelectronic devices

AIM OF EXPRIMENT

The main purpose of this lab is the introduction of different optoelectronic devices, these are those devices which will come across while performing experiments in the lab.

- LED

________________________________________________________________________

________________________________________________________________________

______________________________________________________________________.

- PHOTO TRANSISTOR

________________________________________________________________________

________________________________________________________________________

_______________________________________________________________________.

- FIBER OPTICS

________________________________________________________________________

_______________________________________________________________________

_______________________________________________________________________.

- FUNCTION GENERATOR

________________________________________________________________________

_______________________________________________________________________

______________________________________________________________________.

- OSCILLOSCOPE

__________________________________________________________________

__________________________________________________________________

________________________________________________________________.

- OMEGA TYPE FO-003

_____________________________________________________________________

_____________________________________________________________________

____________________________________________________________________.

EXPERIMENT NO. 2

Introduction to optoelectronic devices trainer

FO-003

EXPERIMENT NO. 3

FIBRE OPTIC TRANSMITTER THROUGH DIGITAL CIRCUIT

THEORY

As you learned in your main course, all fiber optic systems have three major elements:

• Transmitter

• Receiver

• Optical fiber

Figure 1 depicts these major elements. The transmitter and receiver contain smaller elements or building blocks, some of which you should recognize from previous activities. So far with the instructions in this manual we have made a light guide, characterized and terminated optical fibers, and evaluated LEDs and detectors. In this activity we shall investigate one of the last two elements in a fiber optic system the driver for the light source.

1473.eps

Figure1 Basic elements in fiber optic links.

As you have studied, there are two commonly used light sources in fiber optics, LEDs and laser diodes. The drivers covered in this activity are for visible and infrared LEDs. We will not discuss drivers for laser diodes because they are outside the scope of this manual. They can be very sophisticated, complex, and cost thousands of dollars. There are also optical safety considerations when using laser diodes. In more advanced fiber optics classes, or in your job, you will find the information you learned here about driving LED is a good primer for laser diode driver design.

Materials Required

Red LED (IF-E96-blue housing-pink dot)

2N3904

Resistor

Signal generator

Multimeter

Oscilloscope

Solder less breadboard

PROCEDURE

1.	Calculate the resistor value, Rc, needed to permit a current of 20 mA through the LED in Figure 3 when the transistor is saturated. Assume the Vce(sat)=0.2 volts and the Vf for the LED to be 1.8 volts.

2. 	Calculate the maximum value of the base resistor, Rb,needed to drive the transistor into saturation if Vi was connected to + 5 volts. Assume Vbe=.7 volts and hfe(min)= 50.

3. 	Choose resistors from the kit that are closest to the calculated Rc and one-half the calculated Rb. See Table 2 for choices.

Figure2 The two states of digital and

fiber optic systems.

4. 	Assemble the circuit shown in Figure 3 on your solderless breadboard. Use the pin diagrams found to identify device connections.

5. 	Turn on the variable voltage power supply and adjust the output voltage to + 5 volts DC.

6. 	Connect the end of Rb marked Vi to + 5 volts. The red LED should now be on. If not, check the power supply and electrical connections.

7. 	With the multimeter measure the transistor collector-to-emitter voltage and the voltage across the LED, then record the results in Table 1.

8. 	Change Vi from the + 5 volts to ground. The red LED should now be off.

Figure3 Single NPN transistor

switching circuit for driving a fiber

optic LED.

9. 	With the multimeter, measure the collector-to-emitter voltage across the transistor and record the result in Table 1.

RESULTS

Table 1 		Measured data taken from the

circuit shown in Figure 8.3.

| Measurement | Data |
| --- | --- |
| Vce (LED on) |  |
| Vf (LED) |  |
| Vce (LED off) |  |

Analysis & Questions

Is the measured voltage across the collector of 2N3904 transistor in Figure 3 for the LED "on" and "off" compare to what you expected? Why or why not?

With the LED "on" in Figure 3 calculate the "on" current using the measured data in this activity for Vce (sat) and Vf.

EXPERIMENT NO. 4

Analog Signal through the Optical Fiber

Apparatus:

- Function Generator

- Oscilloscope

- Optical Fiber Trainer OMEGA TYPE FO-003

- Optical fiber

Procedure

- Generate a analog Signal from the function generator of 2Vpeak to peak with the frequency of 1KHz

- Apply this analog Signal to the input of the Optical fiber trainer.

- Fix the optical fiber to transmitter and receiver.

- Adjust the gain of the system. Its gain should be 1.

- Take the Output and measure the loss in amplitude of the signal

- Note the input and output measured values in the table shown below

- Draw the input and output waveforms of the signals

- Repeat the above steps by the applying the analog input signal through function generator of 4Vpeak-to-peak with the frequency of 2KHz.

Figure. Sine Wave

##### Results

# Table Readings at 660nm – 1m

|  | 1V | 2V | 3V | 4V |
| --- | --- | --- | --- | --- |
| 100Hz |  |  |  |  |
| 500Hz |  |  |  |  |
| 1KHz |  |  |  |  |

## Table Readings at 850nm – 1m

|  | 1V | 2V | 3V | 4V |
| --- | --- | --- | --- | --- |
| 100Hz |  |  |  |  |
| 500Hz |  |  |  |  |
| 1KHz |  |  |  |  |

WAVE FORMS

#### INPUT WAVE FORM

OUTPUT WAVE FORM

EXPERIMENT NO. 5

Digital Signal through the Optical Fiber

Apparatus:

- Function Generator.

- Oscilloscope.

- Optical Fiber Trainer OMEGA TYPE FO-003.

- Optical fiber.

Procedure

- Generate a Digital Signal from the function generator of 2Vpeak to peak with the frequency of 1KHz

- Apply this Digital Signal to the input of the Optical fiber trainer.

- Fix the optical fiber to transmitter and receiver.

- Adjust the gain of the system. Its gain should be 1.

- Take the Output and measure the loss in amplitude of the signal

- Note the input and output measured values in the table shown below

- Draw the input and output waveforms of the signals

- Repeat the above steps by the applying the Digital input signal through function generator of 4Vpeak-to-peak with the frequency of 2 KHz.

Results:

## Table Readings at 660nm – 5m

|  | 1V | 2V | 3V | 4V |
| --- | --- | --- | --- | --- |
| 100Hz |  |  |  |  |
| 500Hz |  |  |  |  |
| 1KHz |  |  |  |  |

## Table Readings at 850 nm – 5m

|  | 1V | 2V | 3V | 4V |
| --- | --- | --- | --- | --- |
| 100Hz |  |  |  |  |
| 500Hz |  |  |  |  |
| 1KHz |  |  |  |  |

WAVE FORMS

INPUT WAVE FORM

OUTPUT WAVEFORM

EXPERIMENT NO. 6

Optical Fiber Receiver Circuit

Equipment Required

- Photo Transistor

- Resistors

- LED

- Power Supply

- Multimeter

- Solder less Bread board

- Connecting wires

Procedure

- Connect the circuit as shown in the diagram given below

- Apply +5V potential to the collector and emitter should be grounded

- There should be no input at the base. Do remember that base should always be kept open.

- Measure the current properly at the emitter.

- When we apply the light at the base of transistor the current flows through the emitter resulting in glowing the LED.

- Measure the voltage across the Resistor when the light is applied to the phototransistor and when it is kept OFF.

- Measure the current across the Resistor when the light is applied to the phototransistor and when it is kept OFF.

Figure 1 Optical Fiber Receiver Circuit

Results

| Light ON Light OFF | Vcc | IC | IE | VRC |
| --- | --- | --- | --- | --- |

EXPERIMENT NO. 7

TO DETERMINE THE NUMERICAL APERTURE OF OPTICAL SIGNAL

EXPERIMENT NO. 8

STUDY THE OPTICAL (E-O) CHARACTERISTOCS OF FIBER OPTIC 660nm CONVERTER

EXPERIMENT NO. 9

Triangular wave through the Optical Fiber

Apparatus:

  - Communication system trainer KL-100 / ED-2960.

  - Oscilloscope.

  - Optical Fiber Trainer OMEGA TYPE FO-003.

  - Optical fiber.

###### Procedure

- Generate a Triangular Signal from the communication system trainer.

- Apply this Triangular Signal to the input of the Optical fiber trainer.

- Fix the optical fiber to transmitter and receiver.

- Adjust the gain of the system. Its gain should be 1.

- Take the Output and measure the loss in amplitude  of the signal

- Note the input and output measured values in the table shown below

- Draw the input and output waveforms of the signals

- Repeat the above steps by the applying the Triangular input signal through communication system trainer at other carrier amplitudes.

Figure. Triangular Wave

Results:

## Table Readings at 660nm – 5m

|  | 1V | 2V | 3V | 4V |
| --- | --- | --- | --- | --- |
| 100Hz |  |  |  |  |
| 500Hz |  |  |  |  |
| 1KHz |  |  |  |  |

## Table Readings at 850 nm – 5m

|  | 1V | 2V | 3V | 4V |
| --- | --- | --- | --- | --- |
| 100Hz |  |  |  |  |
| 500Hz |  |  |  |  |
| 1KHz |  |  |  |  |

WAVE FORMS

INPUT WAVE FORM

OUTPUT WAVEFORM

EXPERIMENT NO. 10

Amplitude Modulated Signal through the Optical Fiber

Apparatus:

- Communication system trainer KL-100 / ED-2960.

- Oscilloscope.

- Optical Fiber Trainer OMEGA TYPE FO-003.

- Optical fiber.

Procedure

- Generate a AM Signal from the communication system trainer.

- Apply this AM Signal to the input of the Optical fiber trainer.

- Fix the optical fiber to transmitter and receiver.

- Adjust the gain of the system. Its gain should be 1.

- Take the Output and measure the loss in amplitude  of the signal

- Note the input and output measured values in the table shown below

- Draw the input and output waveforms of the signals

- Repeat the above steps by the applying the AM input signal through communication system trainer at other carrier amplitudes.

Figure Amplitude Modulated Signal

Results:

| Input Output | Voltage | Power | Voltage | Power |
| --- | --- | --- | --- | --- |

EXPERIMENT NO. 11

Frequency Modulated Signal through the Optical Fiber

Apparatus:

- Communication system trainer KL-100 / ED-2960.

- Oscilloscope.

- Optical Fiber Trainer OMEGA TYPE FO-003.

- Optical fiber.

Procedure

- Generate a FM Signal from the communication system trainer.

- Apply this FM Signal to the input of the Optical fiber trainer.

- Fix the optical fiber to transmitter and receiver.

- Adjust the gain of the system. Its gain should be 1.

- Take the Output and measure the loss in amplitude  of the signal

- Note the input and output measured values in the table shown below

- Draw the input and output waveforms of the signals

- Repeat the above steps by the applying the FM input signal through communication system trainer at other carrier amplitudes.

Figure. Frequency Modulated Signal

Results:

| Input Output | Voltage | Power | Voltage | Power |
| --- | --- | --- | --- | --- |

EXPERIMENT NO. 12

MAKING A LIGHT GUIDE CIRCUIT

Theory

In this activity you will construct a simple light guide using water and a length of vinyl tubing. The water and vinyl tubing will act as the core, while air will act as the cladding or boundary layer. The experiment will demonstrate how effective even a simple light guide is for coupling energy from a light source to a detector. You will also observe how the light guide can carry light “around a corner” with relatively little loss compared to when light travels in a straight line.

Figure 1 Cross section of an optical fiber with a light ray

traveling down the core.

Materials Required

Red LED 					Paper towels

Phototransistor (T 1 3/4 package) 		Small, shallow, water-tight pan

Vinyl tubing, 15 cm 				Miscellaneous electrical test leads

150 Ω resistor 					Multimeter

Eye dropper 					Distilled Water

Solderless 					breadboard

Single-edge razor blade or sharp knife 		Variable voltage power supply

Procedure

1. 	Using a single-edge razor or sharp knife trim a small amount from the ends of the vinyl tubing so that they are clean and square (90 degrees).

2.	Insert the red flat-topped LED into one end of the vinyl tube. Be sure to insert the LED all the way into the tubing to ensure a tight fit.

3. 	Insert the phototransistor (T 1 3/4 package) into the other end of the vinyl tubing. Push the phototransistor in completely for a tight fit.

4. 	Turn on the variable voltage power supply and adjust the output to + 5 volts DC.

5. 	Set the function of the multimeter to read "Current" on the 2 mA scale.

6. 	On your solderless breadboard connect the electrical circuits as shown . Use the device diagrams found in the to identify anode and cathode on the LED, and collector and emitter on the phototransistor. (The Phototransistor and multimeter circuit will function as an inexpensive radiometer to evaluate the light guide. This type of circuit photo detector/multimeter) will be used as a radiometer throughout this manual.)

Figure 1 Cross section of an optical fiber with a light ray

traveling down the core.

7. 	Light should be visible from the red LED at this point. If not, check the electrical

connections to the LED.

8.	The multimeter should indicate current flow through the phototransistor. If not, check the electrical connections and correct polarity for the phototransistor.

To obtain best results in this activity, you may need to dim the room lights or cover the light guide with a

dark cloth or box. This will minimize the chance of ambient light being captured by the phototransistor, and

Improve the accuracy of your measurements.

9. 	In Table 1 record the current measured by the multimeter (LED ON).

10. 	Disconnect the 150 Ω resistor from the + 5 volt power supply, which will turn the LED off.

11. 	In Table 1 record the current measured by the multimeter through the

phototransistor with the LED off.

12. 	Remove the vinyl tubing, red LED and phototransistor as an assembly from the

solder less breadboard. Pull the red LED

from the vinyl tubing (leaving the phototransistor in), and slowly fill the vinyl tubing with distilled water using

the eyedropper. Do not hurry when filling the tubing; try to put in a drop at a time to avoid leaving any air

bubbles in the tubing. Bubbles will scatter some of the light being transmitted through the water.

13. 	Re-insert the red LED in the vinyl tubing and push in completely for a tight fit to prevent water from leaking

out. Make certain there are no air bubbles inside the tubing between the red LED and phototransistor. Refill as

necessary during the experiment if any water leaks out.

14. 	Re-connect the red LED and phototransistor to the circuit on the solder less breadboard. Re-connect the 150 Ω

resistor to the +5 volt power supply. In Table 2 record the current measured by the multimeter (LED ON).

15. 	Disconnect the 150 Ω resistor from the + 5 volt power supply, which will turn the LED off. In Table 2

record the current measured by the multimeter through the phototransistor with the LED off.

16. 	Gently make a 90-degree bend in the light guide and repeat steps 14 and 15. Be careful to not let any water

leak out from the light guide — refill if necessary. Record the data in Table 3.

17. 	Dip the light guide into a pan

of water. Describe below

what happens to current measured by the multimeter, and what happens to the red

LED light. (It may help to dim the room lights to view the LED light better.)

18. 	Turn off the power supply and return all items to their proper storage containers and locations.

RESULTS

Table 1		Empirical data for 15 cm (6-inch) light guide

with air core.

| LEDs | LED OFF | LED ON |
| --- | --- | --- |
| Red |  |  |

Table 2 		Empirical data for 15 cm light guide with

water core.

| LEDs | LED OFF | LED ON |
| --- | --- | --- |
| Red |  |  |

Table 3 		Empirical data for light guide with 90-degree

bend.

| LEDs | LED OFF | LED ON |
| --- | --- | --- |
| Red |  |  |

Analysis & Questions

What is the amount of light in milliwatts (mW) that falls on the phototransistor when using the red LED with the light guide and water core [assuming the responsivity of the phototransistor to be 50 milliamperes / milliwatts (mA/mW)]? What is it with no water in the core?

Does the light guide send more or less light onto the phototransistor with water in the core? Why?

Did the 90-degree bend significantly change the amount of light hitting the phototransistor? Why or Why not?

EXPERIMENT NO. 13

LOSSES IN OPTICAL FIBER AT 660nm AND 850nm